Jeff95TA’s 1995 Pontiac Trans Am Engine Removal - September 2005

= picture

= part number

(drawer #) = location of parts in bin

- remove hood (drawer #1)

- remove strut tower brace

- disconnect battery

- remove front air dam (drawer #1)

- drain coolant

- remove radiator cap; open bleed screws ; open sill cock

- remove catalytic converter:	 two front nuts (leave on y-pipe studs); loosen clamp

two rear nuts/washers (leave on exhaust pipe)

- remove y-pipe (drawer #2)

- remove block plug  (move mount bolt to get to plug; replace nut) (drawer #2)

- disconnect knock sensor wire  & remove knock sensor  (drawer #2)

- remove intake elbow, MAF, CAI ,

- unplug IAT

- disconnect Optispark air

- unplug MAF

- disconnect secondary air injection hose from CAI

- remove front sway bar bolts/screws

- driver side  - plate over one bolt must be removed ; 2 screws & 1 nut; left front is stud that holds plate (drawer #3)

- passenger side   (drawer #3)

- remove serpentine belt

- discharge A/C; disconnect A/C hose (pg. 1B-3, item #7) from condenser  & compressor  (pg. 1B-3, bolt item #28)    (drawer #4)

- disconnect transmission fluid cooler lines

- one at radiator

- other on line (hose clamp)

- remove lower radiator hose from radiator   & water pump

- remove upper radiator hose from water pump

- remove heater outlet hose from water pump

- remove heater inlet hose from water pump

- remove bypass hose from radiator  & water pump

- remove electrical grounds from right side of engine block   (drawer #5)

- remove shift linkage from transmission

- remove bracket (2 bolts)  - put back on pan

- remove cable from lever assembly

- remove torque arm

- support rear end & remove bolts  from rear (put back in place)

- loosen 2 mount bolts

- match mark driveshaft to yoke & remove   (have to remove driveshaft safety loop - drawer #5); put caps & bolts back on yoke

- remove intermediate steering shaft

- remove clamp & move boot

- remove bolt  from gear assembly   (drawer #6)

- remove shaft from gear assembly

- remove boot

- remove shaft assembly shield

- remove bolt from shaft assembly    (drawer #6)

- remove shaft assembly

- remove two ground straps & screw from driver side frame rail    (drawer #6)

- disconnect electrical connectors for front wheel speed sensors 5E1-178   (leave attached at wheel)

- disconnect on frame rails   (driver) &   (passenger)

- disconnect fuel lines from fuel rail

- loosen filler cap

- relieve pressure at fuel pressure connection

- disconnect fuel lines

- remove from fuel line hold-down ring

- disconnect vacuum line that runs in fuel line loom

- remove accelerator control/cruise control servo cable adjuster assembly

- remove cover

- remove 2 nuts on manifold   (drawer #7)

- rear nut holds a bracket with a hold-down ring  for throttle cable

- disconnect throttle cable

- remove cover nut & cover   (drawer #7)

- remove cable from throttle body & bracket

- note that throttle cable routes under wiring harness

- disconnect brake booster vacuum hose from intake manifold

- disconnect coolant air bleed pipe hose from radiator

- disconnect A/C hose from expansion valve ; plug with plastic bag & tape; note wiring zip tie, plastic clip (drawer #8), & plastic strap

- disconnect A/C lines from dehydrator & remove (have to loosen screw on clamp)

- remove power steering reservoir screw & retainer (drawer #8); reposition reservoir

- remove brake valve assembly, hydraulic modulator/motor pack, & TCS valve assembly (also replacing master cylinder); 12mm lines

- remove fluid from master cylinder

- disconnect front & rear brake combination valve pipe assemblies @ valve & master cylinder (items 31 & 32 on fig. 10, pg. 5-15)

- remove master cylinder (2 nuts - drawer #8)

- disconnect 4 electrical connectors     ;   has a plastic retainer (drawer #8)

- disconnect left  & right  front brake pipes (items 34 & 35 on fig. 10) from valve assembly

- disconnect left  & right  rear brake pipes (items 103 & 102 on fig. 10)

- remove heat shield	- 2 nuts & 1 screw (drawer #9)	- one nut by #1 header

- one screw midway

- one nut at bottom

- remove brake pipe clip (breaks easily) (item 38 on fig. 10): one screw/stud (item 42 on fig. 10)  (same one heat shield screw attaches to) (drawer #9)

- remove traction control brake pressure modulator valve pipe

- remove valve assembly bolt

- remove valve assembly (slide unit to front to disengage tab)

- disconnect wiring harness from traction control valve assembly

- remove 4 bolts (2 front & 2 rear) holding traction control valve assembly/bracket (drawer #10); drop unit out bottom

- reposition traction control throttle cable to clear brake lines

- runs over rear brake pipes

- runs past left side of booster & behind

- disconnect wiring harness on A.I.R. pump   (runs over to main harness on left)

- remove right-hand body pillar trim panel assembly (drawer #11)	- 4 screws on sill trim piece

- 1 screw on speaker pod

- 2 plastic pins on cover &  metal clip

- disconnect three engine wiring harnesses (blue, black, & white) (note the orange retainers on blue & white connectors)

- disconnect evaporator temperature sensor connector

- wiring harness is routed through firewall

- disconnect forward lamp wiring harness connectors

- remove two vacuum lines	-  is attached to the harness  (sits under vacuum connector in clip)

-  is in the way of the harness

- disconnect A/C refrigerant pressure sensor connector

- remove PCM - 2 screws (drawer #2)

- remove other A/C line on expansion valve

- unclip wiring harness hold-downs    (closest to firewall penetration)   (below expansion valve, on A/C lines)

- remove grommet, pull harness thru firewall, place on engine

- disconnect positive lead on alternator   (leave nut on alternator)

- remove zip tie from negative wire on wiring harness

- disconnect battery positive lead at junction block (remove zip tie)

- disconnect battery negative lead at mounting stud

- pull cables out bottom

- drain transmission fluid

- remove front wheels

- place rear wheels on set of old wheels and place jack stands under frame rails

- place straps around lower control arm and disconnect struts from strut tower (Torx bolts are on driver’s side) (drawer #13)

- place jack under K-member and remove slack

- place jack under transmission cross member, remove slack, and remove 4 cross member bolts (drawer #14)

- place dolly under transmission pan

- remove 6 K-member bolts (short bolt is furthest to rear) (drawer #15)

- place another strap to hold steering knuckle

- lower jacks until transmission is on dolly

- put jack under transmission tail & remove dolly

- remove front brake pipe clip (drawer #15)

- lower both jacks (front jack went all the way down); transmission jack was still raised a little

- attach strut tower brace with 3/8” x 1.5” Grade 5 bolts & nuts

- lift body with chain and engine hoist on strut tower brace

- when high enough put jack stands/wood risers under frame and lower car

- remove engine hoist

- wheel engine/transmission out

- attach engine hoist to strut tower brace and put car lower on jack stands

# Text boxes

XX

##

A

B

C

D

E

1

F

H

G

2

3

4

5

I

J

K

L

6

7

M

8

9

10A

10B

N

O

11B

O

12

O

P

13

14A

14B

P

15

Q

R

16

17

18

S

T

U

V

W

19

X

20

V

21

Y

22

Z

AB

AA

AC

25

AD

23L

23R

24

AE

AF

26

AG

AH

AI

27

AJ

AK

AL

AM

28

AN

29

AO

AQ

AP

30

AR

AS

AT

31

32

33

34

AU

34

AV

35

36

AW

37

38

AX

AY

AZ

BA

BB

39

AW

40

AX

BC

41

BD

BF

BH

BE

BG

42

BI

BJ

45

BM

44

43

BK

BL

46

BN

47

BO

48

BP

BQ

49

BR

BS

BT

BU

BV

BW

50

BX

BY

51

BZ

52

BZ

CA

CB

CC

CD

CE

CF

CG

CH

CI

CJ

CK

CL

CM

CN

CO

CP

CQ

CR